## Slide 1: Build your own colorimeter

## Slide 2: What is Colorimetry
"the measurement of colour"
"any technique used to evaluate an unknown colour in reference to known colours".

## Slide 3: What is a colorimeter?
An apparatus that allows the absorbance of a solution at a particular frequency (colour) of visual light to be determined.
Colorimeters hence make it possible to ascertain the concentration of a known solute, since it is proportional to the absorbance.

## Slide 4: The Beer-Lambert Law
The Beer-Lambert law (or Beer's law) is the linear relationship between absorbance and concentration of an absorbing species.

## Slide 5: Current Colorimeters
£3,644 + VAT!
£109 + VAT!

## Slide 6: How do they work?

## Slide 7: So what do you need?
A light source
A light detector
Something to hold it all
A way of measuring the light

## Slide 8: How do you put it together?
Use a cork borer to make holes

## Slide 9: How do you put it together?
Push the LED into a cut-down bung and push it into one end of the hole
Push the LDR the other end of the hole

## Slide 10: How do you put it together?
Connect the LED to a power supply
Connect the LDR to a multimeter and set it to measure resistance.

## Slide 11: Filters
Many experiments do not need filters – the ones we are going to do today for instance
Theatrical lighting gels are a good source of colour filters – you can get free sample packs!

## Slide 12: Choosing Filters
The hard way – look at the absorption spectrum and pick the wavelength that has the highest value
The easy way – use a colour wheel. Look at the colour of your solution and pick a filter of the colour on the opposite side.

## Slide 13: Improving the results
This is a very simple set-up.
It benefits from tweaking the results.
Chart: 
| 1 | 0.5 | 0.25 | 0
Resistance | 3.05 | 2.82 | 2.64 | 2.4

## Slide 14: Improving the results
Excel is very useful for this.
Zero them – so the lowest value becomes zero
Chart: Green Colour v Resistance (Blue Filter)
| 1 | 0.83333333333333359 | 0.66666666666666663 | 0.5 | 0.33333333333333331 | 0.16666666666666666 | 0
Zero Adjusted | 2.15 | 1.83 | 1.55 | 1.21 | 0.88 | 0.54 | 0

## Slide 15: Improving the results
2. Express them as a percentage.
Chart: Iodination of propanone - R% v t(s) for different [HCl]
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240
1M | 100 | 100 | 72.179 | 44.7471 | 30.3502 | 18.677 | 0.58366 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.5M | 100 | 100 | 88.3333 | 76.4583 | 64.375 | 53.3333 | 42.0833 | 31.25 | 20 | 9.5833 | 0.20833 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.25M | 100 | 100 | 93.0018 | 85.8195 | 78.8214 | 71.2707 | 63.9042 | 57.6427 | 51.9337 | 46.4088 | 40.1473 | 33.8858 | 28.1768 | 22.4678 | 17.4954 | 12.3389 | 7.3665 | 2.5783 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.1M | 100 | 100 | 93.0556 | 86.8056 | 81.9444 | 77.4306 | 72.9167 | 69.4444 | 65.2778 | 61.8056 | 58.3333 | 53.8194 | 48.9583 | 44.4444 | 38.8889 | 34.7222 | 30.9028 | 27.0833 | 22.2222 | 18.4028 | 14.9306 | 11.4583 | 7.2917 | 3.4722 | 0